## Slide 1
Digital Logic Design
234262
Alex Bronstein

## Slide 2
Computers Around Us

## Slide 3
Course Goals
Learn how to design logic systems
Learn the design of a simple CPU (MIPS)
Stop worrying and learn to love digital systems 
Notes: Most digital design effort in the industry is non-CPU ASICs
IP cores and fabless semiconductor industry
CPUs are often instanced in complex HW systems

## Slide 4
Short bio
In the Academia:
B.Sc. and M.Sc. in EE, Technion (1998-2005)
Ph.D. in CS, Technion (2005-2007)
Prof., EE@Tel Aviv University (2010-2016)
Prof., CS@Technion (from 2016)
Research interests: computer vision, machine learning, computational geometry, imaging and image processing
In the Industry:
Cofounder and VP Technology, Novafora Inc. (2006-2009)
Cofounder, Invision Ltd. (2009-2012)
Research Scientist & Principal Engineer, Intel Corporation (from 2012)
Cofounder and Chief Scientist, Videocites Ltd. (from 2014)
Notes: Unsystematic knowledge
Practitioner

## Slide 5
Course Staff
Alex Bronstein (lecturer in charge)
Taub 719 bron@cs.technion.ac.il
Chaim Baskin (lecturer)
Taub 700 chaimbaskin@cs.technio.ac.il
Noam Yeffet (TA in charge)
Taub 327 snyefet@cs.technion.ac.il
Tommy Bojan (TA)
Taub 717 tommy.Bojan@intel.com
Alon Gueta (TA)
Taub TBD alon.gueta@campus.technion.ac.il
Aviram Imber (TA)
Taub 213 aviram.imber@campus.technion.ac.il
Bahjat Kawar (TA)
Taub 213 bahjat.kawar@campus.technion.ac.il
Moshe Liechtenstein (TA)
Taub 437 smosesli@cs.technion.ac.il

## Slide 6
Course Formalities
Grade:
25% home assignments
75% final exam
Assignments:
2 “dry” exercises (2.5%)
2 “wet” Verilog coding exercises (10% each)
Passing grade (>54) mandatory in each of the “wet” exercises
Notes: HDL – Verilog! We will learn how to code and see (toy) HW development flow

## Slide 7
Hardware
Notes: Hardware engineer at work?

## Slide 8
Hardware
Notes: A fab worker holding a photolitographic mask

## Slide 9
Hardware
Notes: 99% of logic design is actually this: writing code and running tests

## Slide 10
Hardware Design Flow (ASIC)
Design specs
Architecture
RTL design
Functional verification
Logic synthesis
Floor planning
Placement & routing
Physical verification
Tapeout
Mask tooling
Fabrication
Packaging
Frontend
Backend
Foundry
Technology
library
Static timing analysis
Notes: ASIC = Application specific IC

## Slide 11
Hardware Design Flow (FPGA)
Design specs
Architecture
RTL design
Functional verification
Logic synthesis
Placement & routing
Notes: FPGA = Field programmable gate array

## Slide 12
Software Design Flow
Design specs
Architecture
High-level code
Compilation
Notes: Huge simplification. Tests are ignored

## Slide 13
Software vs. Hardware
Software Hardware
Design cost Low High
Design cycle Fast Slow
Language High-level languages HDL
(Java, C#, C++, C) (Verilog, VHDL)
Code undergoes Compilation Synthesis
Parallelism Usually sequential Inherently parallel
(SIMD, threading, IPC)
Target platforms CPU FPGA or ASIC
(x86,ARM,GPU,DSP) (lots of processes)
Notes: SIMD
Threading
IPC

## Slide 14
Good Engineering Practices
Modularity
Design basic building blocks (modules)
Connect modules together to form another module
A module can be replaced by a new version without affecting the rest of the system
Standardization
Using a library with a small amount of standard modules
Clearly defined functionality and interfaces
Don’t reinvent the wheel
Abstraction
Decomposition of design process into a hierarchy of levels
Hide unnecessary lower-level details

## Slide 15
Abstraction
Simplifies design and understanding of complex systems
A higher level of abstraction is based on the level beneath
A higher level of abstraction hides details of lower levels
Always try to solve problems at the highest possible level of abstraction
Example of abstraction hierarchy:
  High-level language
  Machine language
  Register-transfer level (RTL)
  Gate level, analog electronics
  Physics

## Slide 16
Abstraction vs. Implementation
Abstraction: low level  higher level
Implementation: high level  lower level
Abstraction requires adhering to a certain set of rules to be valid
High-level language: variable
Register-transfer level: register
Gate level: NAND gates
Physics: p-type and n-type MOSFETs

## Slide 17
Abstraction of Digital Systems
Physical Logical
Input: Vin > VIH 1
Output: Vout > VOH 1
Input: Vin < VIL 0
Output: Vout < VOL 0
VIL < V < VIH undefined
Noise margins increase robustness to noise added to signal passing from the output of one component to the input of another
Allows modularity!
VIH
VOH
VOL
VIL
noise
margin
noise
margin
V
Notes: Explain difference between static and dynamic (domino) logic

## Slide 18
Timing
Contamination delay (tCD) – minimum time following input change during which validity of previous output is guaranteed
Propagation delay (tPD) – maximum time following input change after which the validity of new output is guaranteed
VIH
VIL
Vin
t
VOH
VOL
Vout
t
tCD
tCD
tPD
tPD
Notes: Show hazard

## Slide 19
Combinational Logic (CL)
Output = Boolean function of the input
Building blocks:
  Logic gates
  Wires
  Combinational logic sub-systems
Building rules:
  No feedback
  No floating wires (except inputs and outputs)
  Number of inputs each output drives does not exceed fanout limitations
Notes: Give positive and negative examples
Explain fanout

## Slide 20
Static Timing
If inputs to CL system are valid and stable, after settling time, outputs are also valid and stable
Allows resilience to inaccurate analog components
Prevents noise accumulation during signal propagation
Allows cheap mass production of components
OLD
NEW, Stable
OLD
NEW, Stable
OLD
NEW, Stable
INPUT
OUTPUT1
OUTPUT2

## Slide 21
Static Timing
Example: Inverter (NOT gate)
Vin < VIL  Vout > VOH
Vin > VIH  Vout < VOL
VOH
VOL
Vout
VIL
VIH
Vin
Actual components have different analog characteristics due to
Fabrication tolerances
Temperature changes
Supply voltage fluctuations

## Slide 22
Static Timing
Contamination delay (tCD) – minimum time following input change during which validity of all previous outputs is guaranteed
  Components in parallel: min of tCD
  Components in series: sum of tCD
Propagation delay (tPD) – maximum time following input change after which the validity of all new output is guaranteed
  Components in parallel: max of tPD
  Components in series: sum of tPD
Notes: Show components in series and in parallel

## Slide 23
Synchronous Static Memory
Positive edge-triggered D flip-flop (DFF)
Logical characteristic:
Output Q assumes the value of D after CLK rise
Timing characteristic:
If input is held constant tSU before
and tH after clock rise then
old output will stay valid at least tcCQ
and new output will become valid
at most tpCQ after clock rise
D
Q
CLK
NEW
OLD
NEW
CLK
D
Q
tSU
tH
tcCQ
tpCQ

## Slide 24
Synchronous Static Memory

## Slide 25
Synchronous Sequential Logic
State machines
Building blocks:
  Combinational logic modules
  Clocked memory modules
  Wires
Building rules:
  No CL loops unless through at least one memory module
  Clock period long enough to satisfy timing requirements
  All inputs remain stable enough time to satisfy timing requirements
Q
D
CLK
CL

## Slide 26
Finite State Machines (FSM)
CL
U1
Un
…
Y1
Ym
…
X1
Xk
…
X’1
X’k
…
MEMORY
INPUTS
OUTPUTS
PRESENT
STATE
NEXT
STATE
A finite set of states X{0,…,K-1}
k bits represent 2k states
n-bit input U
m-bit output Y
State update function:
X[t+1] = (X[t],U[t])
Output function:
Mealy FSM: Y[t] = (X[t],U[t])
Moore FSM: Y[t] = (X[t])

## Slide 27
FSM Timing
CL
U
Y
X
X’
DFFs
CLK
tpCQ
tPD
tSU
Clock period
T > tpCQ + tPD + tSU

## Slide 28
FSM Timing
CL
U
Y
X
X’
DFFs
CLK
tPD
tSU
Clock period
T > tpCQ + tPD + tSU
Input setup time
tSU(U) > tPD(CL) + tSU

## Slide 29
FSM Timing
CL
U
Y
X
X’
DFFs
CLK
Clock period
T > tpCQ + tPD + tSU
Input setup time
tSU(U) > tPD(CL) + tSU
Input hold time
tH(U) > tH(DFF)- tCD(CL)

## Slide 30
Additional Timing Considerations
Q
D
CLK
Q
D
CLK
Q
D
CLK
Clock skew: clock signal arrives
with different delay to different memories
Clock jitter: clock is not exactly periodic
Asynchronous inputs may violate hold requirement and cause metastability

## Slide 31
Latency and Throughput
Latency: amount of time passing between the beginning of a calculation and its end (input-to-output delay)
Throughput: rate at which calculations are performed (=calculations per unit of time)

## Slide 32
Latency and Throughput
Example: sum of N numbers
∑
MEM
Sequential implementation
Latency = N×t0
Throughput = 1/(N×t0)
∑
∑
∑
∑
∑
∑
∑
Combinational implementation
Latency = log2N×t0
Throughput = 1/(log2N×t0)