## Slide 1
Digital Logic Design
234262
Alex Bronstein
Lecture 2: Pipelines

## Slide 2
Abstraction Hierarchy
Application Software
Operating System (threads, files, exceptions)
Computer Architecture (instruction set)
Micro-Architecture (execution pipeline)
Logic (adders, multipliers, FSMs)
Digital Circuits (gates)
Analog Circuits (amplifiers)
Process and Devices (MOS FET transistors)
Physics (electrons, holes, tunneling, band gap)

## Slide 3
Reminder: CL Timing
Contamination delay (tCD) – minimum time following input change during which validity of previous output is guaranteed
Propagation delay (tPD) – maximum time following input change after which the validity of new output is guaranteed
VIH
VIL
Vin
t
VOH
VOL
Vout
t
tCD
tCD
tPD
tPD
Notes: Show hazard

## Slide 4
Reminder: CL Timing
Contamination delay (tCD) – minimum time following input change during which validity of previous output is guaranteed
Propagation delay (tPD) – maximum time following input change after which the validity of new output is guaranteed
in
t
out
t
tCD
tCD
tPD
tPD
Notes: Show hazard

## Slide 5
Reminder: DFF Timing
Positive edge-triggered D flip-flop (DFF)
Logical characteristic:
Output Q assumes the value of D after CLK rise
Timing characteristic:
If input is held constant tSU before
and tH after clock rise then
old output will stay valid at least tcCQ
and new output will become valid
at most tpCQ after clock rise
D
Q
CLK
NEW
OLD
NEW
CLK
D
Q
tSU
tH
tcCQ
tpCQ

## Slide 6
Latency and Throughput
Latency: amount of time passing between the beginning of a calculation and its end (input-to-output delay)
Throughput: rate at which calculations are performed (=calculations per unit of time)

## Slide 7
Latency and Throughput
Example: sum of N numbers
t0=tPD of each adder
∑
MEM
Sequential implementation
Latency = N×t0
Throughput = 1/(N×t0)
∑
∑
∑
∑
∑
∑
∑
Combinational implementation
Latency = log2N×t0
Throughput = 1/(log2N×t0)

## Slide 8
Hardware Underutilization
∑
∑
∑
∑
∑
∑
∑
t
t0
2t0
0
3t0
∑
∑
∑
∑
∑
∑
∑
4 adders are idle in [t0,3t0]
2 adders are idle in [0,t0] and
[2t0,3t0]
1 adder is idle in [0,2t0]
66.7% “Unemployment”!
INPUT
OUTPUT

## Slide 9
Hardware Underutilization
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
33% utilization

## Slide 10
Can we do better?
Hardware can be better utilized if
The calculation has to be evaluated on many inputs (potentially: an infinite input stream)
System is compute-bound rather than I/O-bound: input throughput is
higher than the calculation throughput
How?
Supply new input after t0 time

## Slide 11
Better Hardware Utilization
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
100% utilization asymptotically
But… violation of CL timing rules!
Input must stay valid until output is produced

## Slide 12
Better Hardware Utilization
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
∑
Solution: Latch intermediate results into registers

## Slide 13
Hardware Underutilization
Assembly Line
Invention erroneously attributed to H. Ford. Earliest instance: Portsmouth Block Mills, ca. 1803

## Slide 15
Wavefront Propagation

## Slide 16
Pipeline
Pipeline: sequential computational process operating simultaneously on multiple computations
Clock period can be lowered to t0 (a little more counting register delays)
New input is supplied at every clock
Asymptotically (infinite input stream):
Throughput  1/t0
Hardware fully utilized
Very common in
  Practically any modern CPU
  Fast computationally-intensive logic such as graphics, DSP, etc.

## Slide 17
Pipeline Timing
∑
∑
∑
∑
∑
∑
∑
a
b
IN
OUT
IN
a
b
OUT
c
c
tCLK
2tCLK
3tCLK
4tCLK
5tCLK
0
CLK
tCLK ≥ tpCQ(REG) + tPD(CL) + tSU(REG)

## Slide 18
Pipeline Design
Naïve approach
  Design CL circuit first
  Break the flow by adding registers until max throughput is achieved
Problem: unbalanced paths!
∑
∑
x
y
z
x+y
x+y+z
∑
∑
xn
yn
zn
xn-1+yn-1
xn-2+yn-2+zn-1
xn-2+yn-2+zn-2
zn-1

## Slide 19
k-Pipeline
k-pipeline is a feed-forward logical circle
  Comprising only CL and registers
  Every path from input to output contains exactly k registers
CL is a 0-pipeline
Pure pipeline is a k-pipeline with only one path from input to output
Usually divided into stages
More complicated pipelines may exist (e.g., with feedback loops or paths of unequal length)

## Slide 20
k-Pipeline Design
Input: CL circuit (0-pipeline) with correct functionality
Output: k-pipeline with correct functionality
Method: iterative application of two rules

## Slide 21
Rule 1: Add Delay
Add a register to every output of the entire system
Same functionality
Result delayed by one cycle
W.l.o.g. can be applied to inputs instead of outputs
k-pipeline
(k+1)-pipeline

## Slide 22
Rule 2: Retiming
For a given subsystem, remove one register from every output and add
one register to every input
Functionally indistinguishable subsystems
Actual evaluation will now occur later
W.l.o.g. inputs can be switched with outputs
k-pipeline
k-pipeline

## Slide 23
Example: Pure Pipeline
0-pipeline
Latency=2T
Throughput=1/2T
T
T
1-pipeline
Latency=2T
Throughput=1/2T
2-pipeline
Latency=4T
Throughput=1/2T
2-pipeline
Latency=2T
Throughput=1/T
T
T
T
T
T
T
RETIME
ADD
ADD

## Slide 24
Example: k-Pipeline
0-pipeline
2T
T
T
Latency=4T Throughput=1/4T
RETIME
ADD
1-pipeline
2T
T
T
Latency=4T Throughput=1/4T
ADD
2-pipeline
2T
T
T
Latency=8T Throughput=1/4T
2-pipeline
2T
T
T
Latency=6T Throughput=1/3T

## Slide 25
Example: k-Pipeline (cont.)
RETIME
ADD
2-pipeline
2T
T
T
Latency=6T Throughput=1/3T
RETIME
2-pipeline
2T
T
T
Latency=4T Throughput=1/2T
3-pipeline
2T
T
T
Latency=6T Throughput=1/2T
3-pipeline
2T
T
T
Latency=6T Throughput=1/2T

## Slide 26
k-Pipeline Timing
Pipeline is a sequential logic circuit
Clock period is determined by
  tCLK ≥ tpCQ(REG) + tPD(CL) + tSU(REG)
  in every path from register to register
Usually, tPD(CL) >> tpCQ(REG), tSU(REG) hence tCLK max{tPD(CL)}
In the example:
tCLK ≥ tpCQ(REG) + max{tPD(A), tPD(C)+tPD(B)} + tSU(REG)
 max{tPD(A), tPD(C)+tPD(B)}
Additionally, hold conditions must be satisfied
tcCQ(REG) + tCD(CL) ≥ tH(REG) (normally tcCQ > tH by design)
In the example: min{tCD(A), tCD(C)+tCD(B)} ≥ tH(REG)
A
B
C

## Slide 27
k-Pipeline Throughput
Ignoring register times tCLK=2T
Non asymptotic throughput:
1 input: 1/2tCLK = 1/4T
2 inputs: 2/(2tCLK+tCLK) = 2/6T
3 inputs: 3/(2tCLK+2tCLK) = 3/8T
4 inputs: 4/(2tCLK+3tCLK) = 4/10T
…
N inputs: N/(2tCLK+(N-1)tCLK) = N/((N+1)2T)
Asymptotic throughput (when N): 1/2T
2T
T
T
Input
Stage 1
N=
0 1 2 3 4 5 6
Output

## Slide 28
k-Pipeline Latency
Clock period tCLK determined by maximum CL delay
If all outputs have registers and k>0:
Latency = k tCLK
If all inputs have registers and k>0:
Latency = k tCLK