## Slide 1
Digital Logic Design
234262
Alex Bronstein
Lecture 3: Memory and Buses

## Slide 2
Abstraction Hierarchy
Application Software
Operating System (threads, files, exceptions)
Computer Architecture (instruction set)
Micro-Architecture (execution pipeline)
Logic (adders, multipliers, FSMs)
Digital Circuits (gates)
Analog Circuits (amplifiers)
Process and Devices (MOS FET transistors)
Physics (electrons, holes, tunneling, band gap)

## Slide 3
Reminder: D Flip Flop
Positive edge-triggered D flip-flop (DFF)
Logical characteristic:
Output Q assumes the value of D after CLK rise
Timing characteristic:
If input is held constant tSU before
and tH after clock rise then
old output will stay valid at least tcCQ
and new output will become valid
at most tpCQ after clock rise
D
Q
CLK
NEW
OLD
NEW
CLK
D
Q
tSU
tH
tcCQ
tpCQ

## Slide 4
Under the Hood
1 DFF = 2×gated D-latches
Based on positive feedback
of inverting gates
~20 transistors / bit of memory
Pros:
Fast!
Cons:
Chip area (=$)
Power

## Slide 5
Memory Array
Many circuits can be shared in
a memory array
N address bits (2N addresses)
M bits word width
Decoder selects and asserts
a wordline
Data stored in bit cells are transferred
to or from bitlines
One word can be accessed at a time
Memories differ mainly by the bit cell structure
N:2N DECODER
ADDR
N
0
1
2N
D0
D1
DM-1
.
.
.
wordline 0
bitline 0
stored
bit cell

## Slide 6
Multi-Ported Memory Array
Allows more than one word to be accessed at the same time
Used for register files and video memories
N:2N DECODER
A1
N
D0
N:2N DECODER
A2
N

## Slide 7
Illustrative Read Cycle
2 read ports: Address A1 onto data output RD1, A2 onto RD2
Read cycle is driven by address line
tRC – read cycle time
tAA – address access time (propagation delay)
tOH – output hold from address change (contamination delay)
RD1
M
A1
N
A2
N
A3
N
WD
N
CLK
WE3
RD2
M
OLD DATA
DATA VALID
A1
RD1
tRC
tAA
tOH

## Slide 8
Illustrative Write Cycle
1 write port: Writes data WD onto address A3 on clock rising edge if write enable WE3 is asserted
tAS – address setup before WE3 is asserted
tWR – write recovery (address hold)
tDW, tDH – write data setup/hold times
RD1
M
A1
N
A2
N
A3
N
WD
M
CLK
WE3
RD2
M
DATA VALID
A3
WD
tDW
CLK
WE3
tDH
tWR
tAS

## Slide 9
Memory Types
Random Access Memory (RAM) – volatile
  Static RAM (SRAM)
  Dynamic RAM (DRAM)
Read-Only Memory (ROM) – non-volatile
  ROM
  Programmable ROM (PROM)
    One-time programmable (OTP)
    Erasable PROM (EPROM)
    Electrically Erasable PROM (EEPROM)
    Flash Memory

## Slide 10
Static Memory (SRAM)
Cross-coupled inverters to store bit
2 access transistors to read/write data
6 transistors / bit
Multiported SRAM is used to implement
register files
Pros:
Fast (but slower than FF)
Cons:
Chip area (but less than FF)
wordline
bitline
bitline

## Slide 11
Static Memory (SRAM)

## Slide 13
Dynamic Memory (DRAM)
Capacitor to store bit
Access transistor to read/write data
Read is destructive
Pros:
Area
Cost
Cons:
Slow (output not actively driven by a transistor)
Power (due to refresh)
More complicated controllers
Row open latencies
wordline
bitline

## Slide 14
Non-Volatile Memory (ROM)
Access transistor: 0 bit
No transistor: 1 bit
Content established at manufacturing
Fuse programmable ROM
(aka one-time programmable, OTP):
  Transistor is present in all cells
  Fuse blown once to program content
wordline
bitline
bitline
bit 0
bit 1
wordline
bitline
bitline
bit 0
bit 1

## Slide 15
EPROM/EEPROM
Floating gate transistor
Programming by application of higher voltage
(hot charge injection into floating gate)
Erasure by
  EPROM: exposing the die to UV light
  EEPROM: applying reverse voltage (electron tunneling from
  floating gate)
wordline
bitline

## Slide 16
Look-up Table (LUT)
ROM can implement any CL function
N-bit address, M-bit word width = N-bit input, M-bit output
Often used for controllers, FSMs, nonlinear transformations
Depending on the function, logic/arithmetic implementation might be advantageous

## Slide 17
System Bus
From Latin omnibus (=“for all”); English plural: buses or busses
A communication system connecting internal components of a computer
Common data highway is cheaper than many point-to-point links
ADDRESS
DATA
CPU
PRIMARY
MEMORY
SECOND.
MEMORY
I/O
CONTROL

## Slide 18
System Bus
Address bus – selects device (and address within)
Control bus – specifies what action the device needs to perform
Data bus – transfers data
ADDRESS
DATA
CPU
PRIMARY
MEMORY
SECOND.
MEMORY
I/O
CONTROL

## Slide 19
Master and Slave
Electrically a bus is a wire (actually, a bundle thereof)
Bus master – device that drives the bus (its output sets the voltage)
Bus slave – device that is driven by the bus (its input receives the signals from the bus)
ADDRESS
DATA
CPU
PRIMARY
MEMORY
SECOND.
MEMORY
I/O
CONTROL
READ
123FA
<DATA>
WRITE

## Slide 20
Tri-State Logic
1
1
1
1
0
BUS
CPU OUTPUT
RAM OUTPUT
X

## Slide 22
Tri-State Logic
EN
EN
Add Enable signal to disconnect output from the bus
When disconnected, the output is floating (high impedance, high Z)

## Slide 23
Tri-State Logic
Tri-state logic can be in 3 states: 0, 1, and Z
Buffers amplify signal, improve fanout and isolate systems
Inverters further invert output
X
Y
E
E X Y
0 0 Z
0 1 Z
1 0 0
1 1 1
X
Y
E
E X Y
0 0 0
0 1 1
1 0 Z
1 1 Z
X
Y
E
E X Y
0 0 Z
0 1 Z
1 0 1
1 1 0
X
Y
E
E X Y
0 0 1
0 1 0
1 0 Z
1 1 Z
_
_
_
_
Tri-state buffers
Tri-state inverters
Active high enable
Active low enable
Active high enable
Active low enable

## Slide 24
Bidirectional Tristate Buffer
Allows to access the bus for reading or writing
to bus
from bus
bus
direction

## Slide 25
Bus Arbiter
A multi-master bus requires an arbiter to decide which master is going
to control the bus at each clock cycle
Arbiter can be centralized (a dedicated circuit) such as in PCI, or
decentralized implementing some handshake protocol

## Slide 26
Direct Memory Access (DMA)
Using the CPU to directly control I/O devices can be very costly
It would be better if an I/O device (e.g., a harddrive) could transfer data directly to/from RAM without the CPU needing to execute any in/out instructions
Direct Memory Access Controller (DMAC) has the capability to become the bus master to control the bus to transfer data between I/O device and memory
CPU sets up the DMAC to transfer a sequence of bytes
DMAC can handle several concurrent transfers (channels) competing over the bus

## Slide 27
DMAC Bus Arbitration
I/O Device
DMAC
Memory
CPU
DMA Request
Hold Request asserted
Hold Acknowledge asserted
DMA Acknowledge
Data transfer via bus
Data transfer via bus
.
.
.
Hold Request deasserted
Hold Acknowledge deasserted
Cycle
stealing