## Slide 1
Digital Logic Design
234262
Alex Bronstein
Lecture 11: Instruction-level parallelism

## Slide 2
Abstraction Hierarchy
Application Software
Operating System (threads, files, exceptions)
Computer Architecture (instruction set)
Micro-Architecture (execution pipeline)
Logic (adders, multipliers, FSMs)
Digital Circuits (gates)
Analog Circuits (amplifiers)
Process and Devices (MOS FET transistors)
Physics (electrons, holes, tunneling, band gap)

## Slide 3
Instruction- (and data-) level parallelism
Exploit parallelism among instructions!
Deeper pipeline to allow more instructions to overlap
  Break instruction to more stages
  Run at a faster clock
Multiple issue: launch multiple instructions at the same clock cycle
  Static: scheduling done by the compiler
  Dynamic: scheduling done at runtime by the processor
Single instruction multiple data (SIMD): vector operations
  Particularly useful when applying the same program to a stream of data such as in multimedia application

## Slide 4
Deeper pipelines
Deeper pipelines and faster clocks
  Example of Intel processors:
  486 Pentium Pentium Pro Pentium IV Core
  Year ’89 ’93 ’97 ‘01-’04 ‘06
  Stages 5 5 10 22-31 14
  Clock [Hz] 25M 60M 200M 2-3.6G 2.9G
  Power [W] 5 10 30 75-100 75
Large branch penalties
Fast clocks are power inefficient
Modern architectures favor multiple lower-frequency cores

## Slide 5
Static multiple issue
Compiler packages instructions into issue slots
Several instructions are launched in a single clock cycle
More hardware is typically required inside the CPU core
Very long instruction word (VLIW) architectures
Common in DSP and embedded processors

## Slide 6
Very long instruction word (VLIW)
Example: static two-issue MIPS (as in some embedded MIPS variants)
One 64-bit instruction packet with two issue slots:
IMEM is 64-bit aligned
Unused slots must be filled with nops
ALU/Branch instruction
Load/Store instruction
0
31
32
63

## Slide 7
Static two-issue pipeline
Address | Instruction | Pipeline stages |  |  |  |  |  | 
N | ALU/branch | IF | ID | EX | MEM | WB |  | 
N+4 | Load/store | IF | ID | EX | MEM | WB |  | 
N+8 | ALU/branch |  | IF | ID | EX | MEM | WB | 
N+12 | Load/store |  | IF | ID | EX | MEM | WB | 
N+16 | ALU/branch |  |  | IF | ID | EX | MEM | WB
N+20 | Load/store |  |  | IF | ID | EX | MEM | WB

## Slide 8
Regular one-issue pipeline (simplified)
Reg
File
IMEM
A
O
MEM
PC
+
4
SX
<<2
+
IF/ID
ID/EX
EX/MEM
MEM/WB
s
t
IM
A
L
U

## Slide 9
Static two-issue pipeline
Reg
File
IMEM
A
O
MEM
PC
+
4
SXIM
<<2
+
IF/ID
ID/EX
EX/MEM
MEM/WB
s
t
IM
A
L
U
+
SX
SXIM
SX

## Slide 10
Static multiple issue
IMEM has 64-bit data bus to read 2 32-bit instructions from a packet in a single cycle
Register file has 2 additional read ports (4 total) and one additional write port (2 total)
Separate adder needed to compute data memory address
Twice more instructions execute in parallel (ideally)

## Slide 11
Static multiple issue
EX data hazard
  add $t0, $s0, $s1
  lw $s2, 0($t0)
Forwarding avoided stalls in single-issue pipeline
Cannot forward ALU result to Load/Store in the same packet
Still one cycle load-use latency, but now next two instructions cannot use load result without stalling
More sophisticated scheduling is needed!

## Slide 12
Data dependencies
for (int* p = A; p>0; p--) {
*p += offset;
}
# $s1 = A
# $s2 = offset
loop: lw $t0, 0($s1) # t0 = array element
addu $t0, $t0, $s2 # add scalar in $s2
sw $t0, 0($s1) # store result
addi $s1, $s1, -4 # decrement pointer
bne $s1, $zero, loop # repeat while $s1!=0

## Slide 13
Data dependencies
# One-issue – 5 cycles/iteration
loop: lw $t0, 0($s1)
addu $t0, $t0, $s2
sw $t0, 0($s1)
addi $s1, $s1, -4
bne $s1, $zero, loop
# Two-issue – 4 cycles/iteration
loop: nop | lw $t0, 0($s1)
addi $s1, $s1, -4 | nop
addu $t0, $t0, $s2 | nop
bne $s1, $zero, loop | sw $t0, 4($s1)

## Slide 14
Loop unrolling
// Original loop
for (int* p = A; p>0; p--) {
*p += offset;
}
// Unrolled in ‘bunches’ of 4 – less branch overhead
for (int* p = A; p>0; p-=4) {
*p += offset;
*(p+1) += offset;
*(p+2) += offset;
*(p+3) += offset;
}

## Slide 15
Loop unrolling
# Unrolled with name dependences - 13 cycles/4 iters
loop: nop | lw $t0, 0($s1)
addu $t0, $t0, $s2 | nop
nop | sw $t0, 0($s1)
nop | lw $t0, -4($s1)
addu $t0, $t0, $s2 | nop
nop | sw $t0, -4($s1)
nop | lw $t0, -8($s1)
addu $t0, $t0, $s2 | nop
nop | sw $t0, -8($s1)
nop | lw $t0, -12($s1)
addu $t0, $t0, $s2 | nop
addi $s1, $s1, -16 | sw $t0, -12($s1)
bne $s1, $zero, loop | nop

## Slide 16
Name dependences
Name dependence (aka antidependence): an ordering forced by the reuse of a name (typically of a register) rather than by true dependence
Register renaming: the renaming of the registers (by compiler or hardware) to remove name dependences

## Slide 17
Loop unrolling
# Unrolled with renaming – 8 cycles/4 iterations
loop: addi $s1, $s1, -16 | lw $t0, 0($s1)
nop | lw $t1, 12($s1)
addu $t0, $t0, $s2 | lw $t2, 8($s1)
addu $t1, $t1, $s2 | lw $t3, 4($s1)
addu $t2, $t2, $s2 | sw $t0, 16($s1)
addu $t3, $t2, $s2 | sw $t1, 12($s1)
nop | sw $t2, 8($s1)
bne $s1, $zero, loop | sw $t3, 4($s1)

## Slide 18
Dynamic multiple issue
Instruction scheduled into issue slots dynamically at runtime
Compiler tries to place instructions a priori into a beneficial order
Superscalar architectures dynamically select instructions to issue based on dependencies or speculations
Out-of-order architectures further allow a blocked instruction not to cause the following instructions to wait
Common in many modern high-performance CPUs

## Slide 19
Single instruction multiple data (SIMD)
Example: MIPS SIMD architecture
32 128-bit vector registers addressed by special instructions
Each 128-bit register can be interpreted as
  4-vector of 32-bit words
  8-vector of 16-bit half-words
  16-vector of bytes
Single instruction operates on the entire vector
W0
W1
W2
W3
H0
H1
H2
H3
H4
H5
H6
H7
B0
B1
B2
B3
B4
B5
B6
B7
B8
B9
BA
BB
BC
BD
BE
BF

## Slide 20
Single instruction multiple data (SIMD)
S0
S1
S2
S3
ws
T0
T1
T2
T3
wt
D0
D1
D2
D3
wd
Syntax: addv.w wd, ws, wt
Semantics: element-wise word vector addition

## Slide 21
Single instruction multiple data (SIMD)
RS
rs
D0
D1
D2
D3
wt
Syntax: fill.w wt, rs
Semantics: fills all vector elements with the content of a GPR

## Slide 22
Single instruction multiple data (SIMD)
RS
rs
D0
D1
D2
D3
wd
Syntax: ld.w wd, imm(rs)
Semantics: reads vector contents from memory
SX(imm)
[addr+0]
[addr+4]
[addr+8]
[addr+12]
addr

## Slide 23
Single instruction multiple data (SIMD)
RS
rs
D0
D1
D2
D3
wd
Syntax: st.w wd, imm(rs)
Semantics: stores vector contents to memory
SX(imm)
[addr+0]
[addr+4]
[addr+8]
[addr+12]
addr